## Slide 1: Black-box testing techniques
Durga Prasad Mohapatra
Professor
Dept. of CSE
NIT Rourkela

## Slide 2: Black-box Testing
Test cases are designed using only functional specification of the software:
  without any knowledge of the internal structure of the software.
For this reason, black-box testing is also known as functional testing.

## Slide 3: Errors detected by black box testing
Black-box testing attempts to find errors in the following categories:
To test the modules independently .
To test the functional validity of the software so that incorrect or missing functions can be recognized.
To look for interface errors. 

## Slide 4
To test the system behavior and check its performance .
To test the maximum load or stress on the system.
To test the software such that the user/customer accepts the system within defined acceptable limits.
Errors detected by black box testing

## Slide 5: Black-box Testing Techniques
There are many approaches to design black box test cases:
  Equivalence class partitioning
  Boundary value analysis
  State table based testing
  Decision table based testing
  Cause-effect graph based testing
  Orthogonal array testing
  Positive-negative testing

## Slide 6: Black-box Testing

## Slide 7: Equivalence Class Partitioning
Input values to a program are partitioned into equivalence classes.
Partitioning is done such that:
  program behaves in similar ways to every input value belonging to an equivalence class.

## Slide 8: Why define equivalence classes?
Test the code with just one representative value from each equivalence class:
  as good as testing using any other values from the equivalence classes.

## Slide 9: Equivalence Class Partitioning
How do you determine the equivalence classes?
  examine the input data.
  few general guidelines for determining the equivalence classes can be given

## Slide 10: Equivalence Class Partitioning
If the input data to the program is specified by a range of values:
  e.g. numbers between 1 to 5000.
  one valid and two invalid equivalence classes are defined.
1
5000

## Slide 11: Equivalence Class Partitioning
If input is an enumerated set of values:
  e.g. {a,b,c}
  one equivalence class for valid input values
  another equivalence class for invalid input values should be defined.

## Slide 12: Example - 1
A program reads an input value in the range of 1 and 5000:
  computes the square root of the input number
SQRT

## Slide 13: Example - 1 (cont.)
There are three equivalence classes:
  the set of negative integers,
  set of integers in the range of 1 and 5000,
  integers larger than 5000.
1
5000

## Slide 14: Example - 1(cont.)
The test suite must include:
  representatives from each of the three equivalence classes:
  a possible test suite can be: {-5,500,6000}.
1
5000

## Slide 15: Example - 2
A program reads three numbers, A, B, and C, with a range [1, 50] and prints the largest number. Design test cases for this program using equivalence class testing technique.

## Slide 16: Solution
1. First we partition the domain of input as valid input values and invalid values, getting the following classes:
I1 = {<A, B, C> : 1 ≤ A ≤ 50}
I2 = {<A, B, C> : 1 ≤ B ≤ 50}
I3 = {<A, B, C> : 1 ≤ C ≤ 50}
I4 = {<A, B, C> : A < 1}

## Slide 17: Solution
I5 = {<A, B, C> : A > 50}
I6 = {<A, B, C> : B < 1}
I7 = {<A, B, C> : B > 50}
I8 = {<A, B, C> : C < 1}
I9 = {<A, B, C> : C > 50}

## Slide 18: Solution
Now the test cases can be designed from the above derived classes, taking
  one test case from each class such that the test case covers maximum valid input classes, and
  separate test cases for each invalid class.

## Slide 19: Solution
The test cases are shown below:

## Slide 20: Solution
2. We can derive another set of equivalence classes based on some possibilities for three integers, A, B, and C. These are given below:
I1 = {<A, B, C> : A > B, A > C}
I2 = {<A, B, C> : B > A, B > C}
I3 = {<A, B, C> : C > A, C > B}

## Slide 21: Solution
I4 = {<A, B, C> : A = B, A ≠ C}
I5 = {<A, B, C> : B = C, A ≠ B}
I6 = {<A, B, C> : A = C, C ≠ B}
I7 = {<A, B, C> : A = B = C}

## Slide 22: Solution

## Slide 23: Example - 3
A program determines the next date in the calendar. Its input is entered in the form of with the following range:
1 ≤ mm ≤ 12
1 ≤ dd ≤ 31
1900 ≤ yyyy ≤ 2025

## Slide 24: Example
Its output would be the next date or an error message ‘invalid date.’ Design test cases using equivalence class partitioning method.

## Slide 25: Solution
First, we partition the domain of input in terms of valid input values and invalid values, getting the following classes:
I1 = { <m, d, y> : 1 ≤ m ≤ 12}
I2 = {<m, d, y> : 1 ≤ d ≤ 31}
I3 = {<m, d, y> : 1900 ≤ y ≤ 2025}
I4 = {<m, d, y> : m < 1}

## Slide 26: Solution
I5 = {<m, d, y> : m > 12}
I6 = {<m, d, y> : d < 1}
I7 = {<m, d, y> : d > 31}
I8 = {<m, d, y> : y < 1900}
I9 = {<m, d, y> : y > 2025}

## Slide 27: Solution
The test cases can be designed from the above derived classes,
  taking one test case from each class such that the test case covers maximum valid input classes, and
  separate test cases for each invalid class.
  The test cases are shown in next slide.

## Slide 28: Solution

## Slide 29: Example - 4
A program takes an angle as input within the range [0, 360] and determines in which quadrant the angle lies. Design test cases using equivalence class partitioning method.

## Slide 30: Solution
1. First, we partition the domain of input as valid and invalid classes as follows:
I1 = {<Angle> : 0 ≤ Angle ≤ 360}
I2 = {<Angle> : Angle < 0}
I3 = {<Angle> : Angle > 360}

## Slide 31: Solution
The test cases designed from these classes are shown below:

## Slide 32: Solution
2. The classes can also be prepared based on the output criteria as shown below:
O1 = {<Angle>: First Quadrant, if 0 ≤ Angle ≤ 90}
O2 = {<Angle>: Second Quadrant, if 91 ≤ Angle ≤ 180}
O3 = {<Angle>: Third Quadrant, if 181 ≤ Angle ≤ 270}

## Slide 33: Solution
O4 = {<Angle>: Fourth Quadrant, if 271 ≤ Angle ≤ 360}
O5 = {<Angle>: Invalid Angle};
However, O5 is not sufficient to cover all invalid conditions this way. Therefore, it must be further divided into equivalence classes as shown in next slide:

## Slide 34: Solution
O51={<Angle>: Invalid Angle, if Angle > 360}
O52={<Angle>: Invalid Angle, if Angle < 0}

## Slide 35: Solution
Now, the test cases can be designed from the above derived classes as shown below:

## Slide 36: Example-5: Intersection of two straight lines
Q. Design B-B test cases for the following program:
The program checks if 2 straight lines intersect and print their point of intersection.
Ans: The straight line may be represented as: y = mx + c
Straight lines are given in the form of (m1, c1) and (m2, c2).
Equivalent classes are as follows:
Case 1: The lines are parallel i.e. m1 = m2
So points are (1, 2) and (1, 5)
Case 2: Coincident lines i.e. m1 = m2 and c1= c2
And points are (2, 3) and (2, 3)

## Slide 37: Example-5 Contd.
Case 3: Lines intersecting at one point i.e.
The points may be (2, 5) and (3, 6).
So there are 3 valid equivalent classes. You may include one more valid equivalent classes
There are no boundary values here.
So, the resultant test suite is:
{{(1, 2),(1, 5)}, {(2, 3),(2, 3)} {(2, 5),(3, 6)}.

## Slide 38: Example-6: Solving quadratic equations
Q. Design B-B test cases for the following program:
The program solves quadratic equations of the form
It accepts 3 floating point values as input and gives the roots, e.g. The input may be (7.7, 3.3 and 4.5).
Ans: Equivalent Classes are as follows:
b2 =4ac inputs are: a= 2.0, b=4.0 and c=2.0
b2 >4ac inputs are a=2.0, b= 5.0 and c=2.0
b2 <4ac inputs are a=2.0, b= 3.0 and c=2.0
Invalid Equation inputs are a=0, b= 0 and c=10.0
Write down the test cases accordingly.

## Slide 39: Example-7: Solving linear equations
Q. Design B-B test cases for the following program:
The program solves linear equations in upto 10 independent variables
e.g. 5x+6y+z=5
10x+2y+5z=20
…………
…………

## Slide 40: Example-7 Contd.
Ans: Equivalent Classes are as follows:
Valid Equivalent Classes
      Many Solution (# var < #eqns)
      No Solution (# var > #eqns)
      Unique Solution (# var = #eqns)
Invalid Equivalent Classes
      Too many Variables (# var > 10)
      Invalid Equation (# var = 0)
      Write down the test cases accordingly.

## Slide 41: Example-8: Intersection of two circles
Q. Design B-B test cases for the following program:
The program finds the points of intersection of 2 circles
Ans: Equivalent Classes are as follows:
r1+r2< distance between(x1, y1) and (x2, y2) i.e. not intersecting
r1+r2= distance i.e. touching at 1 point
r1+r2> distance i.e. intersecting at 2 points
Distance=0 and r1= r2 i.e. overlapping
Distance=0 and r1≠ r2
Invalid circles
Write down the test cases accordingly.

## Slide 42: Example-9: Query Book Option in LIS
Q. Design B-B test cases for the option Query Book using a Keyword (e.g. Author name or title).
Ans: The equivalent classes and the corresponding test cases are as follows:
Not present in catalogue (SE, not present)
Present in catalogue (SE, present, 15 issued, not available)
Present in catalogue (SE, present, 10 issued, 5 available)

## Slide 43: Summary
Discussed the errors detected by black-box test testing techniques.
Explained equivalence partitioning technique with some examples.

## Slide 44
References
Rajib Mall, Fundamentals of Software Engineering, (Chapter – 10), Fifth Edition, PHI Learning Pvt. Ltd., 2018.
Naresh Chauhan, Software Testing: Principles and Practices, (Chapter – 4), Second Edition, Oxford University Press, 2016.

## Slide 45
Thank You